## Slide 1: April Tag Hardware Accelerated Breakdown

## Slide 2: High Level Flow (Hardware/Software)
Image Handler Logic
Image From Camera
Greyscale
Gradient Magnitude
Gaussian Blurring
Ix Difference
Edge Detection
Clustering
Segmentation
Segment Connection
Quad Detection
Quad Decode
Duplication Extraction
Key:
Hardware
Software
Memory
Iy Difference
Gradient Theta

## Slide 3: Image From Camera
Image From Camera
Outside world
AxiVideoStream-RGB888

## Slide 4: Greyscale (Per Pixel)
Greyscale
AxiStream-RGB888
AxiStream-RGBGr8888
AxiStream-Grey32f
OR

## Slide 5: Gaussian Blurring (3x3 Convolution)
Gaussian Blurring
AxiStream-Grey32F
AxiStream-Grey32F
AxiStream-RGBGr8888
AxiStream-Grey4.28
OR
OR
3 Buffer rows
(Needed for the convolution)
AxiStream-RGBGr8888
AxiStream-Grey32f
OR
Notes: Used to take input AFTER normalization. This was removed for simplicity in hardware. The blurring stage will have to be modified to handle an 8-bit unsigned int instead of a float.

## Slide 6: Gradient Differences (1x3 & 3x1 Convolutions)
Ix Difference
Iy Difference
3 Buffer rows
(Needed to keep the differences in sync with one another.)
AxiStream
AxiStream
AxiStream-Grey32F
AxiStream-Grey4.28
OR
AxiStream-32F
AxiStream-S5.27
OR

## Slide 7: Gradient Magnitude and Theta (Per Pixel)
Cordic_Atan2_Coroutine
AxiStream-32F
AxiStream-S5.27
OR
Axi-Angle
Axi-Magnitude

## Slide 8: Memory (DMA-Interrupts)
Memory
Axi-Angle
Axi-Magnitude
Frame Received Interrupt
Convert to float (if necessary)
Axi-Angle
Axi-Magnitude
Angle
Magnitude

## Slide 9: Edge Detection
Edge Detection
Theta32F
Mag32F
Edges[Linked List]

## Slide 10: Clustering
Clustering
Edges[Linked List]
Mag32F
Cluster[VectorMap]

## Slide 11: Segmentation
Segmentation
Cluster[VectorMap]
Mag32F
Theta32F
Segments[Array]

## Slide 12: Segment Connection
Segment Connection
Segments[Array]
In-Place

## Slide 13: Quad Detection
Quad Detection
Segments[Array]
Quads[Array]

## Slide 14: Quad Decode
Quad Decode
Quads[Array]
Tags[Array]

## Slide 15: Duplication Extraction
Duplication Extraction
Tags[Array]
GoodTags[Array]

## Slide 16: Image Handler Logic
AxiVideoStream-RGB888
(from camera)
AXI-32F (Mag)
AXI-32F (Theta)
Image Logic (Start/End of frame)
Convert VideoStream to Stream
Process the Pixel (Norm/Grey)
Memory Logic (Dest Memory)
Filter
Compute Gradients
Comms From CPU (AXI)
(from CPU)

## Slide 17: Image Handler Logic
This logic block will handle converting the AxiVideoStream read in from the camera to first an AxiStream and then to a normal Axi bus when storing it in memory.
The memory address should be given to the hardware block on boot from the CPU so it knows where to store the gradients and other data (I.e size of the image)
The interface between the CPU and the hardware can also be an Axi protocol or some other, simpler serial communication. This is so the CPU can configure and prep the hardware for the incoming images.

## Slide 18: Hardware Pipeline
Since each pixel is read in linearly (row by row), most of the complex processing (gaussian blurring and gradients) cannot be done until 3 rows are completed.
Two options:
  Read the entire frame into memory while grayscaling and normalizing it. Then proceed with simpler logic to have a 3x3 sliding window for blurring and gradients.
  Do all the processing as the image is coming in and handling when certain filters start with logic to reduce the required amount of hardware.

## Slide 19: Hardware Pipeline: Option 1
Grayscaling and normalization can occur as the each pixel is read in as they have no dependency on time.
The original image will be stored in memory alongside the grayscaled + normalized image (grayscaled-only image is not needed)
Once completely read in (EOF is read), then the complex filtering can be started and stored into memory as well.

## Slide 20: Hardware Pipeline: Option 1
Advantages:
  Simpler and easier to implement
  Requires less surrounding hardware/logic
  Memory bus is kept mildly free as R/W operations are disjointed
Disadvantages:
  Slows down when the next frame can be read as it cannot exceed the speed of the complex filtering (can be alleviated with buffering)

## Slide 21: Hardware Pipeline: Option 2
Similarly, grayscaling and normalization can occur as the image is being read in and dumped straight into memory.
A counter must be kept to keep track of the number of rows being read in.
Once 3 rows are read, the complex filtering can read its data from memory.

## Slide 22: Hardware Pipeline: Option 2
Advantages
  Keeps pace with the pixel being read in (with a delay of 3 rows)
Disadvantages
  Lots of memory R/W operations that are overlapping
  May cause slight delay between each pixel being read.

## Slide 23: ArcTangent2
Both AprilTag and RavvenTag use atan2 operation with an input vector.
This poses some design choices to be made as atan2 is complex to implement in hardware
Design Choices:
  Floating point vs Fixed point
  Atan2 algorithm
  Resources vs Speed

## Slide 24: Floating-Point vs Fixed-Point
Both are widely used in embedded applications. With the increase in integrated floating-point units (FPUs), floating-point is becoming readily accessible.
Fixed-Point provides increased and fine-tuned precision depending on the situation.
For this application, it may be better to utilize Xilinx's built-in FPU in hardware and perform operations with that as the Cortex A9 on the Zynq has a built-in FPU.
One can convert from fixed-point to floating-point when transferring the data from the FPGA to the CPU, but this can be skipped if all the operations can be done in floating-point.

## Slide 25: ATan2 Algorithms
There are a wide variety of atan2 algorithms that have been developed as atan2 is a commonly used operation in digital signal processing.
Out of all of them, a CORDIC implementation should be used as it can compute both atan and the magnitude together.
CORDIC is, by design, an iterative process which lends its hand to being able to be implemented with fixed-point arithmetic easily and efficiently.
Iterative processes can be easily pipelined in the FPGA with the cost of redundant hardware.

## Slide 26: Resources Vs Speed
Regardless of whether floating-point or fixed-point is used, or whichever atan2 algorithm is chosen, it all comes down to the debate of resources vs speed.
For this application, we may want to opt for a faster operation since a minimal amount of the algorithm will be done on the FPGA.
The FPGA may also take on more of the algorithm given the latency between the CPU and the FPGA is low if large portions of the algorithm iterative over the image.